## Slide 1: Two-sided Data-driven UWB Error Mitigation for Indoor Localization

## Slide 2: Use case: First responders
Sensors used for localization should be:
Robust against adverse environments (e.g., smoke, haze)
Robust against body parts (e.g., hand/head) motion artifacts
Indoor localization can enhance spatial awareness for
First responders
Wheeled-Robots, drones, …

## Slide 3: Use case: Assisting visual-impaired people
Find a seat in a hall/theatre
Navigate in building
Accurate (decimeter) spatial knowledge is crucial
Cross a road

## Slide 4: Ultra-wideband (UWB) sensors
Commercial devices
Research platforms
Range measurements
Radio pulses
Measure range/distance between 2 sensors
Fine-grained (decimeter accuracy) ranges
Robust to smoke, darkness, …

## Slide 5: Challenging wireless conditions
Indoor environments:
Expect more None-Line-Of-Sight (NLOS) links
Multiple objects reflects UWB signals
Inaccurate range measurements
How to mitigate ranging errors?

## Slide 6: UWB background
Multi-pathed environment
Reflector
Extremely short pulses
(even sub-nanosesond)
Reflector
UWB can differentiate the direct path among multiple travelling paths
Measure Time-of-Flight accurately
Direct path
Reflections

## Slide 7: UWB fail under challenging conditions
Multi-pathed environment
Reflector
Reflector
Obstacle
(e.g., thick wall)
Too weak to be detected
The direct path seems to sink in the noise floor due to an obstacle
Error = 2.8m
Channel Impulse Response (CIR)
Classical thresholding approaches may not work
FPI: First Path Index

## Slide 8: Previous data-driven approaches are not insightful
Which CIR (of poll/response/final packets) should be used?
Can combinations of CIRs perform better?
Initiator
Responder
time
POLL
RESPONSE
FINAL
A typical Double-Sided Two-Way Ranging transaction
Neural net
Error
Corrected Range = Raw_Range – Estimated_Error
CIR

## Slide 9: Example 3 CIRs
Sensor estimated FPIs: error = 2.8m
Hypothetical FPIs: error = 0.0m
Using a single CIR may be sub-optimal
FPI: First Path Index

## Slide 10: Proposed approaches
FMCIR (2 or 3 CIR)
WMCIR (3-CIR)
FMCIR: Fused Multi CIR WMCIR: Weighted Multi CIR
Combine multiple CIRs in a transaction for error mitigation
Wi is obtained from the prior knowledge of protocol
Weighted sum
Assumption:
UWB nodes can execute the neural network, or it can transmit the CIR to a processing node
The UWB nodes use the widely used double-sided two-way ranging scheme

## Slide 11: Dataset
Red dots: Anchor positions in train-set
Blue dots: Anchor positions in test-set
Shaded area: Tag’s free movements
A sample: {poll_CIR, response_CIR, final_CIR}
Range errors in train-set
Range errors in test-set

## Slide 12: Compare different approaches
Using 2 CIRs from both side (◀︎) significantly improves the performance
Using all 3 CIRs (◀︎) further reduces up to 45% range error vs. SOTA (◀︎)
SOTA: State of the art
◀︎
◀︎
◀︎

## Slide 13: Drift mitigation for mmWave-IMU odometer
UWB Tag
Lidar
mmWave Radar
IMU
WMCIR significantly reduces drift effect
Outperforming SOTA
Base odometer (MilliEgo): mmWave radar and IMU for trajectory estimation

## Slide 14: Summary
Systematic studies of efficient uses of CIRs for UWB error mitigation
Proposed two multi-CIR data-driven approaches that outperform SOTA
Created a transaction-level synchronized CIR dataset
Future direction:
Drones used as anchors
Drone formation as an input